## Slide 1: Communication tests with high performance FPGAs
Summary of tests at Lisbon (Cesar Tobon – IFIC-Un. Valencia; Joel Silva, José Augusto, José Silva, Guiomar Evans – INESC-ID / LIP / FCUL – Un. Lisboa)
Equipment:
  Xilinx ML605-Virtex-6 board;
  Xilinx ML507-Virtex-5 board;
  Altera Stratix II GX board;
  Workstations;

## Slide 2: Communication tests: inter-board and board-to-board
ML605-Virtex-6 and ML507-Virtex-5 working full-duplex with no errors (two cross TX-RX simultaneously, common clock from either board or external-Stratix II GX)
Advantage of Virtex-6 over Virtex-5: automatic transceiver instances when multiples GBT links are implemented (in Virtex-5 instantiation must be manual)
Loopback GBT TX-RX implementation in Virtex-6
ML605
Virtex6
ML507
Virtex5
TX
RX
RX
TX
PC
PC
USB
USB
Common clock
(ML605, ML507
or Stratix II GX)
GBT
GBT

## Slide 3: Speed Estimates in Virtex-6 (ISE 12.4 Compiler)
Combinatoric Modules: 4 x Reed-Solomon Decoder (4 modules is maximum possible due to # I/O pins.) Critical I/O path: 2.212 ns
Sequential module: 1 x Scrambler. Max. clock frequency ~800 MHz

## Slide 4: FPGA Resources vs. # of full GBT links